## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26120
Problem Statement Title- Digital Twin for Well-to-Surface Optimization of Cyclic Steam Stimulation and Sucker Rod Pump Operations
Theme- Smart Automation
PS Category- Software
Team ID- TBD
Team Name (Registered on portal)- TEAM ________
Organisation- Oil India Limited | Baghewala field, Rajasthan
“Physics + AI for India’s first cyclic-steam oilfield”

## Slide 2: Digital Twin for CSS and Sucker Rod Pump Optimization
Proposed Solution (Describe your Idea/Solution/Prototype)
A physics-driven AI twin of a Baghewala CSS well that tunes steam cycle and sucker-rod pump together to drive Steam-Oil Ratio down while keeping rod-floating risk safe.
Your Team Name
Detailed explanation of the proposed solution
Digital twin of one CSS well, end to end
Physics: Marx–Langenheim heating, Andrade μ(T), Vogel IPR
Dynamics: rod load, pump efficiency, floating-risk index
ML: XGBoost SOR predictor + risk classifier
Bayesian optimizer returns steam volume, soak, cutoff, pump speed
How it addresses the problem
Replaces manual cycle-by-cycle tuning
Minimises SOR (heavy-oil CSS range 3–8 t/m³)
Warns of rod floating before the pump fails
Sub-second answers for a field 550–600 km from Jaipur
One dashboard: predict, optimize, replay, alert
Innovation and uniqueness of the solution
First twin to co-optimize CSS scheduling with SRP
XSPOC, Lufkin, Weatherford, AVEVA, Kongsberg do one, not both
Tuned to real Baghewala data: 1,150 m deep, 8,000–15,000 cP crude
India’s first CSS well (BGW-8, Dec 2018) as the proving ground
Fully open-source stack — no licence cost to Oil India

## Slide 3: TECHNICAL APPROACH
Technologies to be used: Python 3.13 · NumPy / SciPy · pandas · scikit-learn · XGBoost · scikit-optimize · FastAPI · Plotly · pytest
Methodology and process for implementation: physics engine → 3,000 synthetic cycles → ML emulator → true-physics grid optimiser → dashboard → advisory set-points + operating rule to the operator (SCADA hook planned)
Your Team Name
1 · INPUTS
2 · PHYSICS TWIN twin/
3 · DATA & ML ml/
4 · SERVICE api/
5 · DASHBOARD
field_params.json
rev 12 · real Baghewala
1,150 m · 11,500 cP
@ 50 °C
sat. steam 85–97 kgf/cm²
(307–317 °C at sandface)
19 CSS jobs FY26
Price decks
OIL FY25 $78.09/bbl
FY26 floor $65/bbl
OIL cycle records
CSV: steam_t · soak_days
cutoff · spm · oil_m3
produce_days · peak
CalGEM benchmark
9,692 real CSS cycles (CA)
cycle.py — CSS cycle orchestrator
day by day: inject → soak → produce
water cut as a state (condensate flowback 0.87 → 0.56)
produce ends at rate cutoff OR 3 days of rod float
economics gross + incremental · opex
thermal.py
Marx–Langenheim +
sensible heat
Boberg–Lantz cooldown,
δ computed (PEH 15.70–74)
wellbore loss
ipr.py
composite-radial inflow
μ-scaled cold rate · skin
P_res(t) charge/bleed,
P_current 9.4 MPa
viscosity.py
Walther / ASTM D341 μ(T)
Pal–Rhodes emulsion
(O/W ↔ W/O inversion 0.70,
cap 10×)
srp.py
rod load · buoyancy · drag
on produced stream ·
floating index · liquid-basis
pump capacity ·
stroke 64–144 in · declining
SPM (VFD)
ONE μ(T), TWO FAILURES
cold oil → low inflow (ipr)
AND late-cycle rod float once the
stream turns oil-continuous (srp)
dyno.py
Gibbs 1-D wave equation →
surface card; valve-mechanics
pump card; fault classifier
measured-card classifier (96 %)
generate_data.py
twin/ · 3,000 LHS cycles
6 controls incl. pressure
& stroke · seed 42
train.py — XGBoost
log-oil regressor
R² 0.996
incr. margin / day
R² 0.98 in-envelope
float classifier
AUC 0.9998 (emulator role)
uq.py
1,500 paired Monte-Carlo
16 inputs: skin, water cut,
condensate recovery, prices…
→ p10/p50/p90 · P(better)
both decks
optimize.py
surrogate what-if / UQ
emulator · gp_minimize
recommend_physics.py — decision engine
true-physics 5-D grid: steam,
pressure, cutoff, stroke, SPM
(soak fixed 10 d)
53,592 points · 36 s
FI ≤ 0.6 · aggressive /
conservative
calibrate.py — closed loop (twin/)
bounded least-squares fit of formation water_cut / AOF / thickness
from observed cycles → re-recommend
FastAPI · typed /api/*
/api/uq
runtime
SQLite run history · jobs
Docker / Render · CI
/api/optimize
/api/jobs/{id}
/api/recommend/physics
/api/schedule
/api/calibrate
/simulate → /runs
/api/dyno/{cards,
classify}
dashboard/ · EN / हिं · offline
live / MOCK auto-detect
Overview
recommendation: 5 set-points +
operating rule · incremental
₹/day · UQ range · P(better)
Recommendation
Bayesian optimiser job and the
physics-verified point, side by side
P(float) gate < 0.3 · run history
stage → confirm → load
no controller is contacted
Model basis
equations · coverage matrix ·
validation · calibrate · field view
Simulator
cycle replay: water cut & float index ·
computed & measured dyno cards ·
ISA-101 alarm
6 · VALIDATION RING
CalGEM 2021
field SORs 3.47–8.24;
model sits inside
BGW-8 published
first-cycle uplift 5–6×
SOR 3–8 (literature band)
236 tests pass
+ 2 declared gaps: soak;
cold-well pumpability
Self-audit
external tech. review 27 Sep
10 findings, 8 fixed
OIL data request
per-cycle field records
→ calibrate.py loop
Operator
reviews and
confirms
(advisory)
BGW well
CSS job +
sucker-rod
pump
LEGEND
data flow
μ(T) coupling
feedback loop
validated by
closed loop: calibrate.py
re-fits these params

## Slide 4: FEASIBILITY AND VIABILITY
Analysis of the feasibility of the idea
Physics is settled: Marx–Langenheim (1959), Andrade, Vogel (1968)
Field parameters published: 1,150 m depth, 8,000–15,000 cP at 50 °C
Steam at 280–305 °C and 60–70% quality — normal CSS practice
De-risked at this very field: India’s first CSS, BGW-8, Dec 2018
Open-source stack, laptop-scale compute, ~4 weeks to a live API
Your Team Name
Potential challenges and risks
No public Baghewala SOR history to train on
Poor-to-fair reservoir: porosity below 10%
Physics model can drift from real well behaviour
Extreme viscosity makes pump behaviour non-linear
Operator trust in an automated set-point
Strategies for overcoming these challenges
Train on 3,000 physics-generated cycles, deterministic seed
Recalibrate on Oil India historical data at the finale
Parameter-sweep sanity tests on the physics modules
field_params.json as the single source of truth per well
Advisory mode first — the engineer approves every set-point

## Slide 5: IMPACT AND BENEFITS
Potential impact on the target audience
Oil India CSS operators at Baghewala — 52 wells drilled, 33 operational, 19 CSS’d in FY2025-26
Every avoided rod-pump workover saves $15k–$50k (industry-typical)
Output already scaling: 218 t (FY17) → 43,773 t (FY26) — the twin scales with it
Benefits of the solution (social, economic, environmental, etc.)
Economic: less steam fuel burned per barrel produced
Environmental: lower energy and GHG intensity per barrel
Social / safety: rod-floating alerts catch the failure mode behind most SRP workovers
Strategic: an indigenous twin for India’s first cyclic-steam asset, portable to future CSS wells
Your Team Name
Prototype v1 simulation — to be validated on OIL field data.
SOR 1.50 → 0.88 t/m³ (−41.3%) across 3,000 synthetic cycles — self-audited, physics v2 recalibration in progress; literature benchmark for optimisation-driven SOR cuts is >20%.

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
Marx, J. W., & Langenheim, R. H. (1959). Reservoir heating by hot fluid injection. Trans. AIME, 216, 312–315.
Vogel, J. V. (1968). Inflow performance relationships for solution-gas drive wells. J. Petrol. Tech., 20, 83–92.
Gibbs, S. G. (1963). Predicting the behavior of sucker-rod pumping systems. J. Petrol. Tech., 15, 769–778.
Andrade, E. N. da C. (1930). The viscosity of liquids. Nature, 125, 309–310; ASTM D341 viscosity–temperature standard.
SPE-23APOG-535203 (2023). Case study for enhancement of production of heavy and highly viscous crude oil using an electrical downhole heater — Baghewala depth, API and viscosity data.
Oil India Limited — Rajasthan Fields (Baghewala / BGW-8 CSS) https://www.oil-india.com/rajasthan-fields ; production and well-count figures from OIL annual reports.
Competitive landscape (docs/research/landscape.md): XSPOC, Lufkin SAM/SROD, Weatherford ForeSite, Schlumberger, AVEVA, Kongsberg Kognitwin — none couples CSS scheduling with SRP optimization.
Your Team Name