## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26120
Problem Statement Title- Digital Twin for Well-to-Surface Optimization of Cyclic Steam Stimulation and Sucker Rod Pump Operations
Theme- Smart Automation
PS Category- Software
Team ID- TBD
Team Name (Registered on portal)- TEAM ________
Organisation- Oil India Limited | Baghewala field, Rajasthan
“Physics + AI for India’s first cyclic-steam oilfield”

## Slide 2: Digital Twin for CSS and Sucker Rod Pump Optimization
Proposed Solution (Describe your Idea/Solution/Prototype)
For Oil India's Baghewala field — India's first cyclic-steam wells: a digital twin that recommends the steam, pump and stop settings for each cycle, and tells the engineer why.
Your Team Name
Detailed explanation of the proposed solution
How it addresses the problem
Innovation and uniqueness of the solution
Links (fill in before submission)
Every steam cycle, the twin re-plans
the well from first principles —
heat, thick oil, the rod pump.
One well, simulated day by day: inject → soak → produce
Tracks heat, viscosity, water cut and rod loads
Inputs: field parameters + Oil India's cycle records
Output: 5 settings + an operating rule, with a range
Field view: which of the 33 wells gets steam next
Today's cycles are tuned by experience;
the twin adds the physics
and keeps the engineer in charge.
Manual steam and pump choices → one checked plan
Rods that float late in the cycle → slowed, then pulled
Steam wasted on cold oil → less steam per m³ of oil
No field data yet → every assumption tagged and ranged
Engineer reviews, confirms, then loads — advisory only
Steam and pump treated as one system —
because one thick oil
causes both failures.
Couples the steam cycle to the rod pump — rare in tools
Rod float predicted from falling water cut, late in the cycle
Computed dynamometer card + a measured-card checker
Self-audited: 3 physics bugs found and fixed before judging
Offline, English + Hindi, no licence cost — built for the field
Live dashboard:
https:// ________________
Demo video:
https:// ________________
GitHub repository:
https:// ________________

## Slide 3: TECHNICAL APPROACH
Technologies to be used: Python 3.13 · NumPy / SciPy · pandas · scikit-learn · XGBoost · scikit-optimize · FastAPI · Plotly · pytest
Methodology and process for implementation: physics engine → 3,000 synthetic cycles → ML emulator → true-physics grid optimiser → dashboard → advisory set-points + operating rule to the operator (SCADA hook planned)
Your Team Name
1 · The well
2 · Digital twin
3 · Smart search
4 · Dashboard
5 · Operator
What the operator gets
What it leads to
Oil India's heavy-oil well:
steam goes in,
oil comes out.
Baghewala: 1,150 m, 11,500 cP
Oil India cycle records (CSV)
Band check vs California data
A computer copy
of the well —
heat, thick oil, the pump.
Heat flow (Marx–Langenheim)
Thick oil: less flow + stuck rods
Pump loads, rod-float risk
Tries 13,000 plans
in about 3 minutes,
keeps the safe ones.
Physics grid: 12,936 plans
Fast what-if model (XGBoost)
Best / worst case (1,500 runs)
Shows the best plan
in plain words,
English and Hindi.
4 pages, works offline
Computed pump card (dyno)
Upload records → twin re-fits
Decides.
Nothing is sent
to the well automatically.
5 settings + an operating rule
Review, confirm, then load
Field view: which well next
Real cycle records come back → the twin re-learns
How much steam
& pressure
Pump speed
& stroke
Slow, then stop,
before the rods jam
Less diesel
per barrel
A stop rule
for the rods
Every plan
with a range
Built on published physics · benchmarked against a California steam-ratio band · 263 automated tests

## Slide 4: FEASIBILITY AND VIABILITY
Feasibility and viability — a working prototype, its known gaps, and how each gap closes with Oil India's data.
Your Team Name
Analysis of the feasibility of the idea
Potential challenges and risks
Strategies for overcoming these challenges
Roadmap
Built and running today —
published physics,
real field numbers.
Real Baghewala inputs: 1,150 m, 11,500 cP
Steam 85–97 kgf/cm², 60–70 % quality (published)
Inside real field bands (uplift 5–6×, CalGEM)
Runs on a laptop · deployable API + Docker
Some numbers stay assumptions
until Oil India
shares its data.
No public per-cycle Baghewala records
Skin, water cut, condensate return unknown
Rod float depends on emulsion behaviour
Marginal at $65/bbl; negative net of royalty + cess
Every assumption is tagged,
given a range,
and re-fitted from data.
Data request to Oil India ready (10 items)
Calibration loop: 10 cycles → re-fit in minutes
Uncertainty shown as a range, not one number
Advisory mode first · control hook later
Now: prototype,
263 tests, live demo
Oct: Oil India data,
calibrate the twin
Finale: field-checked
recommendations
Pilot: one well,
advisory mode
Team: Chemical Engineering + Software, MNIT Jaipur · open-source stack, no licence cost to Oil India

## Slide 5: IMPACT AND BENEFITS
Impact and benefits — what changes for Oil India's operators, and what we honestly do and do not claim yet.
Your Team Name
Potential impact on the target audience
Benefits of the solution (social, economic, environmental, etc.)
Assumptions to confirm with Oil India
The plan: 1,000 t steam · 89 kgf/cm²
64-in stroke · start 4.5 spm ·
slow at the float limit, then pull.
Steam per m³ of oil: 3.3 → 2.8 t (−14 %), same policy
Beats our assumed baseline in 84–96 % of runs
₹ gain ₹0–5k/day — set by the VFD's minimum speed
Drive slows the pump at the float limit, then pull
Field view: which well gets steam next
Economic
Less steam per barrel:
3.3 → 2.8 t/m³ (−14 %)
23 % less steam · 11 % less oil
₹ gain hinges on OIL's VFD floor speed
A range is shown, never one number
Environmental
Every tonne of steam burns
71 kg of diesel
Fewer tonnes of steam per m³ oil
Less diesel and CO₂ per barrel
No wasted pumping after float
Social & operational
Operators keep control;
the twin explains itself
Plain words, English and Hindi
Rod failures not priced yet ($15–50k)
Open source — skills stay with OIL
Synthetic data today — the first real
cycle records re-fit the twin in minutes
Cash-positive in about half of scenarios
at OIL's FY25 price (vs a shut-in well)
Break-even at $65/bbl; negative net of
royalty + cess — OIL's price deck decides
VFD minimum speed and pull criterion set
the ₹ gain — both on our data request
Scales with the field: 218 t (FY17) → 43,773 t (FY26) of heavy oil · 19 steam jobs in FY26 · one twin per well

## Slide 6: RESEARCH AND REFERENCES
Everything we used is public and cited — physics from the 1950s–80s, field facts from Oil India and SPE, benchmarks from California's regulator.
Your Team Name
Details / Links of the reference and research work
Links (fill in before submission)
Marx & Langenheim (1959). Reservoir heating by hot fluid injection. Trans. AIME 216.
https://doi.org/10.2118/1266-G
Boberg & Lantz (1966). Thermally stimulated well rate — via SPE PEH ch. 15 (Prats).
https://petrowiki.org/PEH:Thermal_Recovery_by_Steam_Injection
Vogel (1968). Inflow performance relationships for solution-gas drive wells. JPT.
https://onepetro.org/JPT/article/20/01/83/163252
Gibbs (1963). Predicting the behavior of sucker-rod pumping systems. JPT 15.
https://doi.org/10.2118/588-PA
ASTM D341 viscosity–temperature charts (Walther); Pal & Rhodes (1989) emulsions.
https://www.astm.org/Standards/D341.htm
API Spec 11E / RP 11L — pumping-unit ratings and rod-string design.
https://www.api.org/products-and-services/standards
SPE-23APOG-535203 (2023). Baghewala heavy oil: depth, API, viscosity, heater case.
https://onepetro.org/SPEAPOG/proceedings-abstract/23APOG/2-23APOG/535203
Yasin et al. (2022). Scientific Reports 12:11086 — Baghewala-1 reservoir properties.
https://doi.org/10.1038/s41598-022-14831-5
Oil India Ltd — Rajasthan fields (BGW-8 CSS); investor presentation (realised price).
https://www.oil-india.com/rajasthan-fields
CalGEM (2021). Annual Report of the State Oil & Gas Supervisor — field steam-oil ratios.
https://www.conservation.ca.gov/calgem/Documents/2021%20CalGEM%20Supervisor%20Annual%20Report.pdf
Inside Climate News (2022) mirror of CalGEM injection data — 9,692 cyclic-steam records.
https://github.com/InsideClimateNews/2022-09-ca-kern-oil-water
Landscape: XSPOC, Lufkin SAM/SROD, ForeSite, AVEVA — none couples CSS with the pump.
https://www.lufkin.com/solutions-services/srod/
Live dashboard:
https:// ________________
Demo video:
https:// ________________
GitHub repository:
https:// ________________
Every link is clickable in this PDF · full list with notes in the repository (docs/research/references.md)