## Slide 1: TECHNICAL APPROACH
Technologies to be used: Python 3.13 · NumPy / SciPy · pandas · scikit-learn · XGBoost · scikit-optimize · FastAPI · Plotly · pytest
Methodology and process for implementation: physics engine → 3,000 synthetic cycles → ML emulator → true-physics grid optimiser → dashboard → advisory set-points + operating rule to the operator (SCADA hook planned)
Your Team Name
1 · The well
2 · Digital twin
3 · Smart search
4 · Dashboard
5 · Operator
What the operator gets
What it leads to
Oil India's heavy-oil well:
steam goes in,
oil comes out.
Baghewala: 1,150 m, 11,500 cP
Oil India cycle records (CSV)
Checked vs 9,692 real cycles
A computer copy
of the well —
heat, thick oil, the pump.
Heat flow (Marx–Langenheim)
Thick oil vs heat (Walther)
Rod loads + rod-float index
Tries 53,000 settings
in 36 seconds,
keeps the safe ones.
True-physics grid, 5 controls
Fast what-if model (XGBoost)
Best/worst case (Monte-Carlo)
Shows the best plan
in plain words,
English and Hindi.
4 pages, works offline
Computed pump card (dyno)
Upload records → twin learns
Decides.
Nothing is sent
to the well automatically.
5 settings, incl. stop rule
Review, confirm, then load
Field view: which well next
Real cycle records come back → the twin learns
How much steam
& pressure
Pump speed
& stroke
When to stop before
the rods jam
Less diesel
per barrel
Safer pump
More oil
per cycle
Built on published physics · checked against real field data · 236 automated tests